## Slide 1: Real Time Systems – SS2016 Prof. Dr. Karsten Weronek Faculty 2 Computer Science and Engineering
Introduction
What does Real-Time computing mean?

## Slide 2: Basic model for a Real-Time-System
Technical System
Actuating-System
Measuring-System
Computer-System
Real-Time-System
external System
internal System
nach Dieter Zöbel, Echtzeitsysteme Grundlagen der Planung, Springer-Verlag Berlin Heidelberg, 2008, ISBN 978-3-540-76395-6
Δe
r
r+Δe ≤ d
t
d
r : earliest start time
d : latest end time
Δe : max. processing time
Sensor System
Actuating Elements

## Slide 3: Introduction: What is Real-Time
Transformation of input data is processed by the speed of arrival. ("xy is Real Time\; xy 2 MP3-encoder,rendering-engine, . . . )
Hermann Kopetz: “A Real Time computer system is a computer system in which the correctness of the system behavior depends not only on the logical results of the computations, but also on the physical instant at which these results are produced." (Real Time Systems, 1999, S. 2)
Jane Liu: ”. . . a Real Time system is required to complete its work and deliver its services on a timely basis." (Real Time Systems, 2000, S. 1)

## Slide 4: Introduction: RTS
Procedures and methods for
  Development
  Implementation
  Analysis
If (computer-)systems which ar subject to a
„Real Time constraint“,
e.g. operational deadlines from event to system response

## Slide 5: Introduction
What is Real Time?
This means:
  Correctness and
  Execution time
of the results are guaranteed.
In non-Real Time Systems only the correctness
of the result is guaranteed (and sometime not even that).
In other words:
A RTS will also guarantee that a certain deadline is met.

## Slide 6: Criteria or RT-computing
There three types of RTS:
Hard: Missing a deadline is a total system failure (airbag in car).
Soft: The usefulness of a result degrades after its deadline, therby degrading the system‘s quality of service. (warning systems).
Firm Infrequent deadline misses are tolerable but may degrade the system‘s quality of service. The usefulness of a result is zero after ist deadline. (car: ignition-point-optimizer for motor)

## Slide 7: Classification of Real Time Systems
  Consequence of missing deadline
  Relaibilty and fault tolerance
  Distribution: centralised or distributed RTS
  Interactive or autonomic system
  Hierarchical or flag system
  Time-driven or event-driven RTS
  Cyclic or asynchronous scheduling

## Slide 8: Embedded Systems
RT-Systems often constitute Embedded Systems:
„Embedded computers are defined to be those where the computer is used as a compontent within a system: not as a computing engine in ist own right. […]“
(Jim Cooling: Software Enginnereing for RTS, 2003, S. 12, Pearson Education)
The computer is not a computer itself, but part of a system.
In other words embedded systems are central and part of the overall system.
(e.g. a missile control)

## Slide 9: Embedded Systems
Complex interaction with the environment and other Embedded Systems
Often operated autonomously
High requirments on reliability
Replace mechanical systems (e.g. regulator, stabiliser, controller)
HW/SW-Code design: System on a chip (SoC)
Usage of processor often not visible
Normaly working under RT constraints
Repair cost higher than new system